## Slide 1: Problem
Three people, verbal to paper
Paper emailed to groups
Transpose paper to excel
Copy/paste into Well View

## Slide 2: Design
Cheaper
Pipe Data: Two person job (one less than current)
Faster
No paper
One Time Collection, no transposing
Better
Accuracy
Data available for import/export, reports in near real time

## Slide 3: Solution
Web API (OData): to collect and expose data WellView, PowerBI, etc
Mobile App: paired with rugged, Bluetooth enabled Laser Measuring device (used on location)
Web App: manual entry of non-pipe related equipment, re-order run, export, in CSV
Notes: Architecture (PaaS: host API, Web app, Db)
  Mobile App. Xamarin IOS / Android: SQLite
    Collect data via Bluetooth enabled Laser
    Online or Off (Auto Sync)
  Web API 2 (OData): Azure
  Web App: Angular 4: Azure
  SQL Server: Azure

## Slide 4: Laser Measurement: onsite Workflow
Fill In repeat data
Gather Pipe Length
Gather Thread Length
Backer board placed flush to female end of a joint
Recorder aims laser to ‘shoot’ inside pipe (leaser flush to male end)
App records max measurement returned from laser
Mobile App saves data
Recorder: positions laser to outside pipe and places a backer board at thread end and records measurement
Notes: Mobile App: (Pipe Measurement)
Enter initial data collection run; Metadata (well, pad, OD, Grade)
Team of two:. One with laser (recorder), one with backer board)
Each team member aligns at each end of a single joint
Measure Pipe Length:
Backer board placed flush to female end of a joint
Recorder aims laser to ‘shoot’ inside pipe (leaser flush to male end)
App records max measurement returned from laser
Measure thread length
Recorder: positions laser to outside pipe and places a backer board at thread end and records measurement
Mobile App saves and resets for next entry
Repeat step 1.2 – 2.4

## Slide 5: Future
Uniquely identifying pipe on the rack:
Add disposable RFID tag to pipe when measuring: used for order, Adding an RFID scanner below the Rig Floor: (Above BOP) to track order in the hole, (also will help id and track pipe with anomalies that would not be ran in.
CBA:
one less person to collect onsite data.
no manual entry (can if needed): save time both onsite and in office.
reduce data latency, improve quality.
Architecture is extensible and scalable